## Slide 1: ISTC PROJECT PROPOSAL № 3609: EXPERIMENTAL INVESTIGATION OF FLOW PULSATION EFFECTS ON BURNOUT IN RPV EXTERNAL COOLING SYSTEM (EXPULS)
Presented by V. Granovsky
A.P. Alexandrov Research Institute of Technology
12 CEG -SAM Meeting
Sept 11-13, 2007 St. Petersburg

## Slide 2: Problem
  IVR concept is used in:
  - current projects (AP-600, АР - 1000, VVER - 640)
  - advanced projects (APR - 1400)
  - modernization (VVER - 440)
  Absence of DNB at the vessel external cooling is compulsory for IVR
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 3: Problem (2)
Experimental data and correlations for CHF versus water mass velocity, subcooling and surface inclination angle are obtained for conditions of vessel external cooling.
The CHF value can be affected by flow oscillations. This has been observed during DNB experiments under water boiling in pipes. This effect has not been studied yet for IVR.
The factor causing oscillations growth is outlet hydraulic resistance for two-phase flow (e.g. slot channels, local hydraulic resistances etc.)
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 4: Objectives
Experimental determination of influence of cooling water flow oscillations on CHF value at the external surface of reactor vessel
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 5: NITI tests on DNB at the external surface of reactor vessel
14 – water ; 5 – helium ; 6 – nitrogen ; 7 – (1)
- Kutateladze
(1)
=180-
The effect of inclination angle
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg
Saturated liquid

## Slide 6: NITI tests on DNB at the external surface of reactor vessel (2)
Forced circulation of coolant
Effects of mass velocity and subcooling were studied separately
Bottom model– slice-geometry, scale 1:1
“Hot spot” method
Test facility PETLYA
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 7: NITI tests on DNB at the external surface of reactor vessel (3)
1, 2, 3 – PETLYA ; 1– =0; 2 – =27; 3 – =90;
4 – ULPU; 5 – «Gidropress»; 6 – (2)
(2)
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg
Generalization of CHF data
Effect of mass velocity and subcooling

## Slide 8: NITI tests on DNB at the external surface of reactor vessel (4)
Test section is the same as in PETLYA test facility
Natural circulation of coolant
Circuit height is 7m
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg
Test facility KEDR

## Slide 9: NITI tests on DNB at the external surface of reactor vessel (5)
1 – forced circulation;
W=50…350 kg/(m2s); Р=0.14…0.17 MPа;
2 – natural circulation;
W=80…250 kg/(m2s); Р=0.15…0.17 MPа;
3 – open circulation circuit
qcr, MW/m2
-
0
.
1
2
-
0
.
1
0
-
0
.
0
8
-
0
.
0
6
-
0
.
0
4
-
0
.
0
2
0
.
0
0
0
.
5
0
1
.
0
0
1
.
5
0
2
.
0
0
2
.
5
0
-
1
-
2
-
3
X
=27
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg
Comparison of CHF experimental data for forced and natural circulation

## Slide 10: Flow oscillations in the test facility KEDR
Subcooled water in the upper tank
Low-frequency oscillations
Flow oscillations are caused by periodic boiling evolution, flow rate increase, suppression of boiling with subcooled water and etc
The process is well described in the KORSAR-code
0
500
1000
1500
2000
0
1
2
3
4
5
0
500
1500
2000
350
360
370
380
390
KEDR
calc
exp
KEDR
calc
exp
exit
time, s
time, s
Temperature, K
Flow rate, kg/s
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 11: Flow oscillation in the system of VVER- 440 vessel external cooling
Vessel cooling by gravity water flow
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 12: Flow oscillation in the system of VVER-440 vessel external cooling (2)
Calculation results by KORSAR code
G, kg/s
G, kg/s
t, s
t, s
G =28 kg/s
Flow reversal with volume boiling at the slot channel inlet
Detail
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 13: Flow oscillations in the system of vessel external cooling
Oscillations could reduce CHF value
Characteristics of oscillations depend on circuit geometry and coolant parameters
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 14: Basis for project EXPULS
Model of VVER-1000 vessel bottom
KEDR test facility
Potentials for transforming KEDR test facility into the system of gravity water flow
Computer code KORSAR
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 15: Project tasks
№ | Task | Pers*day
1 | Pretest calculations. Preparation of experimental test facility. Testing of experiment procedure. Refinement of experimental matrix | 1020
2 | Tests: DNB in natural circulation circuit | 1360
3 | Tests: DNB under gravity flow conditions | 1780
4 | Verification of computer codes | 1490
 |  | 5650
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 16: Expected project results
Experimental data on CHF at flow pulsations
Correlations between the intensity of flow pulsations and the CHF value
Verification of RELAP5mod3.2 and KORSAR/В1.1 computer codes
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 17: Application of results
Expansion of application area of RELAP and KORSAR computer codes
Verification of other thermal-hydraulic computer codes, for instance, CATHARE, ATHLET
Design of the systems for external cooling of reactor vessel and justifying IVR of core melt
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 18: General project information
The project is carried out by NITI
Project manajer – Dr. Yu. Migrov
Participants – 20 persons including 13 weapon scientists (5 PGD) and engineers
Duration – 24 months
Requested funding – $ 184,000
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg

## Slide 19: Conclusion
NITI has the experience of experimental studies of DNB and computer code application for modeling thermal hydraulics in the systems of vessel external cooling
Project EXPULS will give new knowledge about DNB peculiarities under flow oscillations
12 CEG -SAM MEETING
Sept 11-13, 2007 St. Petersburg