## Slide 1: RISK ASSESSMENT OF THERMAL REACTOR ACCIDENT WITH MAXIMAL REPRODUCTION OF FISSILE MATERIALS
Institute of Atomic Energy
National Nuclear Center
Republic of Kazakhstan
Kotov V.M., Kotov S.V.

## Slide 2: PROBLEMS OF THE MODERN ATOMIC ENERGETICS
  1. Short lifetime of the “Big Atomic Energetics”
  (BAE, W > 5000 GWt) if the known types of the thermal reactors are used with the explored reserves of a cheap uranium.
  Lifetime ~ 40 – 60 years. This time can be increased when the closed cycle is used.
  2. Necessity of full conversion of the explored reserves of the cheap uranium if BAE will be developed on the fast neutron reactors
  AES power limitation. High radiation danger. High cost of the uranium enrichment work.
  Fuel conversion time ~ 40 – 50 years.
  3. Support of the weapon materials proliferation
  Uranium enrichment. Spent fuel conversion.
  Risk can be lowered when the fuel with the small concentration of fission materials is used.

## Slide 3: WAYS TO IMPROVE THERMAL REACTORS
1. LWR(BWR) spent fuel usage for the CANDU charge
2. Thorium raw usage in the thermal reactors.
3. Campaign burn increasing at expense of uranium enrichment.
4. Closed cycle technology usage.
5. Paired work with the fast neutron reactors.

## Slide 4: MEASURES FOR INCREASING OF PART OF THE RAW URANIUM USAGE AND THORIUM ENTRAINMENT IN WORK:
1. Technology of zone superposition
The reactivity integral of the campaign must be equal to zero
2. The closed cycle with the balance of all fuel nuclides, apart from 235U, 238U, 232Th
The fissionable elements concentration optimum is on the level from 0.7 to 1.3%
The materials with the minimal neutron loss
The enrichment of the materials by the isotopes with small absorption cross-section
4. Additional neutron sources from the “n-2-n” reaction
The beryllium block in the FA
5. Uniform loading of the fuel elements in the FA
6. Thermonuclear reactor usage for the 233U generation

## Slide 5: CALCULATION METHOD RAW MATERIAL USAGE QUANTITY DEFINITION

## Slide 6: GENERAL ELEMENTS HEAVY WATER REACTOR

## Slide 7: HEAVY WATER REACTOR FA

## Slide 8: CALCULATION RESULTS opened cycle
Heat transfer material Н2О D2O D2O
FA type 36 fe 36 fe 20 fe + Ве
Fuel mass, t 79.12 79.12 43.96
n flux, ×1013 cm-2s-1 3.4 5.8 5.8
Period of campaign, hours 14000 18000 26000
Thermal power, MWt 656 1125 749
Raw material usage, % 0.8 1.8 2.3
n loss in fission products, % 4.13 7.54 8.45
n loss in constr. materials, % 12 3.75 2.15

## Slide 9: CALCULATION RESULTS closed cycle
Raw material type U U+Тh
FM concentration, % 0.71 1.1
Period of campaign, hours 37000 60000
n flux, ×1013 cm-2s-1 5.8 5.8
Thermal power, MWt 749 1160
Raw material usage, % 6.05 11.52
n loss in fission products, % 10.4 12.3
n loss in constr. materials, % 2.5 1.6

## Slide 10: FUEL TECHNOLOGIES COMPARISON raw material - uranium

## Slide 11: REACTORS REQUIREMENTS IN RAW MATERIALS

## Slide 12: About the safety of the introduced technology
Small concentration of the fission materials in the fuel makes fuel cycle safe in regard to nuclear accident.
Reactivity integral adjacency to zero in campaign, lack of strong absorbers in reactor provides nuclear safety basics.
However, accident situations characteristics on that type of reactors were not calculated.
It is desirable to attract specialists, which are directly researching that type of problems.
Safety characteristics estimation of that type of reactor will help to speed up it’s further development

## Slide 13: CALCULATION VARIANTS
Reactors types:
- Power boiling with Н2О;
- Power boiling with D2O;
- Power with metallic heat transfer material (Sn, Sn+Pb+Bi);
- NHP with heavy water heat transfer material;
- Power with limited number of the fuel exchange in campaign;
- Power with the maximal level of raw fuel material usage (100 %);

## Slide 14: CALCULATION VARIANTS
Additional measures:
Channels grid optimization
- Emergency heat removal input through the Be insert
Channel geometry optimization
Nitride fuel with high thermal conductivity
(enriched by 15N)

## Slide 15: EQUIPMENT LOCATION VARIATIONS
AES equipment disposition on the one level. Reactor hall with protective containment isolation.
2. Underground AES location.
3. AES equipment disposition on the two levels. Reactor hall on the lower level.
4. AES equipment disposition as in p.3. Creating a system of the reactor equipment emergency capsulation

## Slide 16: References:
1. V.M. Kotov, S.V. Kotov, L.N. Tikhomirov. Possibility to Use Thermal Reactor with Full Use of Uranium and Thorium Raw //Atomic Power- 2003. Т. 95, Issue 5, pgs. 338 - 346. (in Russian).
2. V.M. Kotov. Full Use of Uranium Raw Materials for Thermal Channel-Type Reactors. //NNC RK Bulletin. Issue 3 (23), September 2005, pgs. 10-17. (in Russian).
3. V.M. Kotov, S.V. Kotov, Irkimbekov R.A. Study of High-Power Channel Reactors Breeding Potential. // NNC RK Bulletin. Issue 3 (23), September 2005, pgs. 18-23. (in Russian).
4. V.M.Kotov, S.V.Kotov, Zh.S.Takibaev, L.N.Tikhomirov. Liquid-salt channel-tipe reactor with dynamic loading and core superposition. / Plasma Devices and Operations. Vol. 13, No. 3, September 2005, 213-221.