## Slide 1: Overview of SARNET Research Priorities and links with ISTC Programmes and CEG-SAM B. CLEMENT (IRSN), K. TRAMBAUER (GRS) presented by P. GIORDANO (IRSN)
CEG-SAM meeting
Clamart, France, March 8-9, 2006

## Slide 2: SUMMARY
Brief review of SARNET project
Links with ISTC programmes and CEG-SAM
Status on SA Research Priorities WP activities

## Slide 3: Brief review of SARNET project (1/2)
Resolution of still pending questions that are important for reactor safety
Optimised use of available resources and competences throughout Europe
Knowledge transfer for safety application
Preserve the competence (capitalize on the knowledge)
200 researchers, 20 phD….
Main objectives :
  18 Countries, 49 organizations
    18 Research Organizations
    10 Universities
    11 Industry Organizations
    4 Utilities
    6 Safety Authorities or Technical Supports
SARNET
Severe Accident Research NETwork of excellence

## Slide 4: Brief review of SARNET project (2/2)
ASTEC
Corium
J.M. Bonnet (CEA)
Containment
L. Meyer (FzK)
Source Term
T. Haste (PSI)
PSA2
R&D Priorities
K. Trambauer (GRS)
Experimental Data Base
Requirements (CPU…)
Tests of methodologies
Models
Models
Develop. priorities
Position / State of the Art
Qualification
Resolution of still pending questions that are important for safety
Definition of a reference plan on research priorities, periodically updated (1st version = EURSAFE PIRT conclusions)

## Slide 5
Modalities of interaction between CEG-SAM and EC-SARNET are defined in document entitled “Interaction between EC-SARNET and CEG SAM activities”, endorsed by the CEG-SAM at its 7th meeting in Cologne on February 28th - March 1st, 2005 and by the EC-SARNET Governing Board on 18 March 2005 in Paris
ISTC Project proposals are transmitted by CEG-SAM to SARNET topical coordinators in charge of the concerned field (CORIUM, CONTAINMENT and/or SOURCE TERM)
  EVAN project proposal sent by P. Hoffman (secretary CEG-SAM) to T. Haste (SARNET SOURCE TERM Topical coordinator)
  INVECOR and PARAMETER project proposals received by J.M. Bonnet (SARNET CORIUM Topical coordinator)
Links with ISTC Programmes and CEG-SAM (1/2)

## Slide 6: Links with ISTC Programmes and CEG-SAM (2/2)
Concerned SARNET topical coordinator organises consultation among SARNET members and prepares technical advice for CEG-SAM . Example :
  EVAN proposal received for review in mid-December 2005, it has been placed on ACT and comments from ST members invited ; placed as an agenda item at 2nd ST annual review meeting (1-2nd Feb. 2006)
  No comment from partners up to the meeting ; at the 2nd ST annual review meeting, a description of the EVAN proposal (including introductory information on ISTC and overview of other ISTC projects) was given by D. Bottomley (ST member) ; only comments from CIEMAT expressed. They will be reported by DB to CEG-SAM.
  At the 2nd ST annual review meeting, a very brief description of VERONIKA proposal was also given by D. Bottomley (ST member)
  It has also been noticed that ISTC 1648.2, may be relevant to FP release during reflood : ISTC web address given to ST members
CEG-SAM considers SARNET advices as inputs to prepare recommendations to ISTC Governing Board

## Slide 7: Status on the SARP WP activities (1/3)
1st review of SARP work (18 months period, presented at EMSAR – Nov.05):
  EURSAFE methodology has been proven as adequate
  Most of the gaps are being closed by actions carried out by SARNET partners
  A few gaps not covered by current (or to be initiated) R&D activities have been already identified :
    CORIUM : Coolability of particulate debris bed in case of reflooding – insufficient validation of existing models because of the lack of multi-D experimental data (ERI 1.2)
    CORIUM : Integrity of RCS, distribution of decay heat, containment bypass (ERI 1.5.)
    CORIUM : Ex vessel corium coolability – scale effects not adequately addressed (ERI 2.2 & 2.4)
    CONTAINMENT : Dynamic and static behaviour of containment, crack formation, FP leakage (ERI 3.5.)
    SOURCE TERM : Characterisation and quantification of fission product release during core reflooding – virtually no data on real irradiated fuel (ERI 5.5.)
  Up to now no resolved issue has been recognized
  A strategy has been developed to :
    Close the issue
    Initiate reorientation of research items
    Launch new research items

## Slide 8: Status on the SARP WP activities (2/3)
Outcomes of last SARP meeting (22nd Feb. 2006) :
  A presentation on Links with ISTC was prepared (B. Clément and K. Trambauer)…but not given due to lack of time ! Among the Content, information on links between EC-SARNET and actual ISTC Projects & New Project Proposals to be discussed by CEG-SAM in March 2006 was intended to be given
    #833.2 (METCOR-2) link with EC-SARNET/CORIUM
    #1950.2 (CORPHAD-2) link with EC-SARNET/ CORIUM
    # 1648.2 (VVER-QUENCH) link with EC-SARNET/ CORIUM, SOURCE TERM
    # 2936 (Reactor Core Melting) link with EC-SARNET/ CORIUM
    # 2916 (CHESS) link with EC-SARNET/ CORIUM
    # 3194 (PARAMETER) link with EC-SARNET/ CORIUM
    # 1265 (INVECOR) link with EC-SARNET/ CORIUM
    # 3345 (EVAN) link with EC-SARNET/ CORIUM, SOURCE TERM
  Synthesis of recommendations from SARNET Advisory Committee and from EC review have been provided and discussed
  A few New or Re-oriented Issues proposals (from Topical areas) have been submitted, for SARP team voting

## Slide 9: Status on the SARP WP activities (3/3)
CORIUM
  New cladding material
  MCCI: Radial / axial spreading of melt
CONTAINMENT
  Hydrogen distribution
  Direct containment heating
SOURCE TERM
  Resuspension in the circuit
  Interaction of PARS with iodine
  Ruthenium behaviour in the containment

## Slide 10: CORIUM (WP09-1 EARLY) : New cladding materials
Rationale for the decision to be taken
  Data on oxidation kinetics, mechanical behaviour etc. under SA conditions (T>1200°C, reflood) are only available for the classical cladding materials.
  New cladding alloys were optimised for operation conditions.
  Proof of reasonable behaviour under SA condition has to be given
Assessment by the SARP team
  Thermal mechanical behaviour of new cladding materials are particularly an issue of design based accidents and should be investigated in this area.
  Differences in the mechanical strength and oxidation kinetics appear minor and do not justify specific experimental research beyond the existing work scope of WP09‑1 (hydrogen generation and fuel rod collapse).
  Beside this the mechanical properties (strain/stress data) should be measured or provided by the industry.
  => additional research not retained

## Slide 11: CORIUM (WP11-2 EXCORE) : Axial / radial melt spreading
Rationale for the decision to be taken
  Tendency for larger radial than axial ablation of siliceous concretes.
  Radial walls are molten through before the basemat.
  Depending reactor design, there can be spreading either in a dry compartment or inside a water pool, with the risks of rapid steam formation
Assessment by the SARP team
  Issue is very plant specific. Enhanced radial erosion may result in loss of structural support of the RPV or melt ingression into water pools.
  Radial melt erosion would not endanger the containment integrity and thus not constitute a high safety and risk importance
  Subsisting large uncertainties do not justify additional R&D effort.
  The consequences of potential enhanced radial erosion on severe accident management should be assessed.

## Slide 12: CONTAINMENT (WP12-2 CAM): Effect of mitigation systems on H2 distribution
Rationale for the decision to be taken
  The efficiency of recombiners is directly affected by thermal and concentration stratification of the atmosphere in the containment.
  Large uncertainties remain in modelling condensation under impinging conditions and/or in the presence of non-condensable light gases.
  The effect of sprays on the mixing of the atmosphere and on the reduction of the hydrogen risk have to be assessed.
Assessment by the SARP team
  Effects of PARs and spray on the hydrogen distribution: only minor changes of the research objectives are necessary for WP12-2.
  Experimental data base sufficient for further model development.
  The model development might be performed in the frame of the WP12-2 (Containment atmosphere mixing) or WP03 (ASTEC assessment).
  Item is assessed as minor reorientation or extension of existing research and development work.

## Slide 13: CONTAINMENT (WP13-2 DCH) : Combustion of H2 jets in the containment
Rationale for the decision to be taken
  The rate of combustion determines the time scale of heat transfer to the atmosphere and thereby the peak pressure.
  Pressure loads under predicted in CFD calculations without setting parameter for the combustion rate arbitrarily.
  Combustion codes (COM3D, REACFLOW) can be validated by means of SETs and then used to extrapolate to different length scales.
  Those results can be used to establish correlations for DCH-codes (CFD and lumped parameter codes).
Assessment by the SARP team
  Effects of ejection of melt containing metallic components combined with steam on the containment pressure due to hydrogen deflagration/detonation: safety and risk imp.
  Investigations fit well into the objectives of WP13-2 and only minor changes of the research objectives are necessary (extended item).
  The experimental data base for hydrogen burns during DCH seems not to be sufficient for further model development particularly for scaling effects.
  Some confirmatory work with limited effort to be performed in the frame of DCH issue.

## Slide 14: SOURCE TERM (WP15 AEROB) : Mechanical resuspension
Rationale for the decision to be taken
  If deposition inhibition and multilayer or monolayer resuspension are not modelled, decontamination capabilities of pipes, of the secondary side of a dry steam generator or of cracks/leakage paths in the containment wall are significantly (non-conservatively) overestimated.
  Generally the codes/models over predict the deposition and fail to describe the transient behaviour of deposit remobilisation
  New experiments (PECA, ARTIST, VTT-DEPOS) are being performed to supplement the data base
Assessment by the SARP team
  Medium safety and risk significance
  State of knowledge not to be evaluated and a new issue is not initiated
  Improvement of models could be performed in the frame of WP15 or WP03
  Check the data base regarding mechanical resuspension of reactor typical deposits

## Slide 15: SOURCE TERM (WP16 CONTCHEM): Effect of FP heat-up in PARs on ST
Rationale for the decision to be taken
  Major potential iodine and other FP compounds embedded in containment aerosol particles (i.e., CsI, AgI; InI, CdI2) decompose under the high temperatures reached during this transport through the recombiner units.
  Aerosol distribution towards smaller sizes
  Experimental investigations are intended by IRSN and a cluster is planned for JPA3 for test interpretation and model development.
Assessment by the SARP team
  Vote on the safety and risk importance for the source term (2.37) and on the lack of knowledge (2.37).
  Perform calculations about the kinetics of decomposition and recombination of aerosols and FPs to estimate the additional source of volatile FPs for existing PARs under consideration of the timing of SAM.
  Perform small scale tests beyond RECI under typical reactor accident conditions to explore the effect of recombination of volatile species.

## Slide 16: SOURCE TERM (WP16 CONTCHEM) : Behaviour of Ruthenium in the containment
Rationale for the decision to be taken
  Significant release of volatile Ru under oxidizing conditions.
  Small amounts of volatile Ru (0.1% of Ru inventory in the fuel) contribute significantly, up to 10%, to possible external radiological consequences one month after the accident.
  The experimental data base needs to be extended for release from irradiated fuel (HBU and MOX) and transport of Ru, and to be established for the behaviour of Ru in the containment for the model development.
Assessment by the SARP team
  Vote on the safety and risk importance for the source term (2.62) and on the lack of knowledge (2.87)
  Review the existing data base to estimate the amount of volatile Ru in the containment under consideration of specific accident sequences and conditions (WP16)
  Perform SETs to complete the data base for the release (WP14-1 OXIDEN) and transport (WP14-2 HITEMP) of volatile Ruthenium.